settn[i] / (index in dlg = i + 1)	Description	Details
(maxset%)	String to search channel titles for to attempt to automatically identify force channel
(maxset% + 1)	String to search channel titles for to attempt to automatically identify EMG channel
0	Default number of reps
1	Flag debug mode	(0: no, 1: yes)
2	Delete temporary channels	(0: no, 1: yes)
Force onset: First pass
3	Force onset included in analysis
4	Min time between threshold crossings	(0: no, 1: yes)
5	Hysteresis
6	Expected number or thresholds in sequence that are required to return the expected number of repetitions for thi s not to be rejected as noise
FIR low-pass filter parameters
7	Toggle of low-pass filtering of the force data (1	(0: no, 1: yes)
8	Filter corner frequency	yes, 0
9	Filter Transition width
Force onset: Second pass
10	Number of SD multiples to be exceeded for level to be regarded as no longer quiescent
11	Size of time window to calculate SDs over
12	Amount of time to move the SD calculation window by each time
13	Amount of time prior to identified force onsets to search for quiescent period
14	How far from the threshold a waveform can move and be rejected as noise
15	Minimum time between threshold crossings to except as valid
16	Percentile over which to calculate mean SD (to avoid noise spikes and initial onset slope)
Force onset: Final pass (Low-pass differentiator)
17	The frequency that the signal will start to be attenuated at
18	How much higher than the corner frequency will maximum attenuation be achieved
Peak force find
19	Toggle whether peak force is found or not	(0: no, 1: yes)
20	Time window to search from force onset for peak force
21	Minimum time peak must meet excursion criteria to be excepted as valid
22	How far from the threshold a waveform can move and be rejected as noise
Rate of force development (ROFD)
23	Toggle whether ROFD is calculated or not	(0: no, 1: yes)
24	The percentage of force range to be used as the START of ROFD calculation zone
25	The percentage of force range to be used as the END of ROFD calculation zone
26	How far from the threshold a waveform can move and be rejected as noise
27	Minimum time between threshold crossings to except as valid
28	Time period after peak to include in search for relaxation thresholds
29	Which times to carry out manual checking on before completing analysis	0: All, 1: Fail, 2: None